## Slide 1
Head/Helmet Contact Force Characterization in Combat Helmet Systems
D'mitra Mukasa, Michael Marchev, Turner Jennings1, Sinan Müftü1, Rouzbeh Amini1,2
1 Department of Mechanical and Industrial Engineering, Northeastern University, Boston, MA
2 Department of Bioengineering, Northeastern University, Boston, MA

## Slide 2: Background - Current Combat Helmet Technology
Head/Helmet Contact Force Characterization in Combat Helmet Systems
NEU Young Scholars Program 2023 - August 3, 2023

## Slide 3: Background - Traumatic Brain Injury (TBI)
A TBI is a family of brain dysfunction caused by an outside force, usually a violent blow to the head, in our case; a projectile or explosive shrapnel
Head/Helmet Contact Force Characterization in Combat Helmet Systems
NEU Young Scholars Program 2023 - August 3, 2023
Notes: Not Classifiable – there are triage criteria which are used to classify TBIs but some combinations do not have a formal classification

## Slide 4: The Problem
Development of higher performance helmet materials relies heavily on numerical simulation.
Current simulations fail to construct a fully representative model.
It is unknown how pre-compression changes behavior of the padding upon impact.
Head/Helmet Contact Force Characterization in Combat Helmet Systems
NEU Young Scholars Program 2023 - August 3, 2023
Cai et al., Appl Bion Biomech, 2020
Notes: Get a little more specific --> talk about sizing --> we don't know exactly how helmet fit affects forces etc.

## Slide 5
Head/Helmet Contact Force Characterization in Combat Helmet Systems
NEU Young Scholars Program 2023 - August 3, 2023
Research Aims
Create experimental testing setup to measure contact force between the helmet and head in combat helmets
1.0
Test the effects of head size, demographics, and chinstrap on helmet contact forces
2.0
Calibrate pressure sensors for combined pressure/bending on helmet pads
1.1

## Slide 6: Abstract
Motivation
Previous studies on impact mechanics of combat helmets have failed to consider pre-compression of helmet padding under normal use conditions.
Our Goal:
Obtain experimental data on helmet/head contact forces to determine relationship between head size, helmet size, and pad pre-compression.
Head/Helmet Contact Force Characterization in Combat Helmet Systems
NEU Young Scholars Program 2023 - August 3, 2023
Notes: sl

## Slide 7: Methods
Objective: Estimate pad compression on helmets (S, M, L, XL) by taking readings of contact force on subject heads at rest while wearing helmets
Head/Helmet Contact Force Characterization in Combat Helmet Systems
NEU Young Scholars Program 2023 - August 3, 2023
Assemble helmets with pads
Record pressure data with and without chinstrap
Record participants’ age, sex, head length, width, and circumference
Sew pressure sensors on pads and run through Arduino
Calibrate mapping between voltage output and pressure applied through repeated measurements with known forces

## Slide 8: Methods - Calibration
Diagram of pressure sensor calibration setup
Calibration setup in use
Head/Helmet Contact Force Characterization in Combat Helmet Systems
NEU Young Scholars Program 2023 - August 3, 2023
Helmet shell
Helmet pads
Force Gauge
Z-axis stage

## Slide 9: Methods – Assembled Helmet
Head/Helmet Contact Force Characterization in Combat Helmet Systems
NEU Young Scholars Program 2023 - August 3, 2023
Pressure sensors
Data connection
Arduino board
Helmet pads
Helmet shell
Helmet measurement setup

## Slide 10: Results - F vs. M Unstrapped
Head/Helmet Contact Force Characterization in Combat Helmet Systems
NEU Young Scholars Program 2023 - August 3, 2023
No significant difference between male and female participants when helmet is unstrapped

## Slide 11: Results - F vs. M Strapped
Head/Helmet Contact Force Characterization in Combat Helmet Systems
NEU Young Scholars Program 2023 - August 3, 2023
Contact forces with chinstrap significantly higher on male participants (p<0.05) when chinstrap applied

## Slide 12: Results - Strapped vs. Unstrapped All
Head/Helmet Contact Force Characterization in Combat Helmet Systems
NEU Young Scholars Program 2023 - August 3, 2023
Contact forces with chinstrap are significantly higher than without the chinstrap (p<0.05)

## Slide 13: Results – Helmet Fit vs. Contact Pressure
Head/Helmet Contact Force Characterization in Combat Helmet Systems
NEU Young Scholars Program 2023 - August 3, 2023
Tighter fit loosely correlated with higher contact force, more data needed

## Slide 14: Future Work
Head/Helmet Contact Force Characterization in Combat Helmet Systems
NEU Young Scholars Program 2023 - August 3, 2023
Our data will be used to calibrate finite element simulations considering pad pre-compression in the future.
These simulations will be used to design granular materials capable of greater shock absorption.

## Slide 15: Acknowledgments
Center for STEM Education
Claire Duggan, Executive Director
Jennifer Love, Associate Director
Claire Stipp and Yassine Souabny, YSP Coordinators
Nicolas Fuchs, Program Manager
Mary Howley, Administrative Officer
ARL Soldier Protection Program CA#W911NF2120208.

## Slide 16: Head/Helmet Contact Force Characterization in Combat Helmet Systems
pre-compression is naturally present and brought on by the weight of the helmet, the fit of the head within the pads, and use of the chinstrap
Prior studies on ballistic impact with combat helmets have failed to considered pre-compression of padding [1,2]
A characterization of contact forces has not been previously attempted
(A) (B) (C)
Obtained S, M, L, XL Advanced Combat Helmets with Oregon Aero pads and assembled as instructed; sewed pressure sensors onto all pads with connection to Arduino
Recorded demographic data (age, gender);measured head length, width, and circumference; documented contact forces with and without chinstrap
Current combat helmets consist of an exterior fiber composite shell with an interior soft foam padding. This foam layer provides additional protection by absorbing shock transferred from helmet shell to skull through compression upon impact. Existing research does not consider pre-compression that occurs while wearing the helmet; the accuracy of these models used to model force propagation is therefore limited. This affects predictions of the risk of impact-induced traumatic brain injuries. Four different size helmets have been instrumented with contact pressure sensors on the interior padding system. We will use these instrumented helmets to measure head-helmet interface contact forces on volunteer users. We hypothesize that interface forces will change depending on whether the user fastens the helmet strap and that male and female volunteers will additionally contrast due to statistical differences in head size. The experiments conducted will be used to calibrate finite element simulations of impacts on a helmeted head to develop higher-performing energy absorbing materials capable of reducing the risk of impact-induced traumatic brain injury.
[1] Tan, L.B. et al., Int J Impact Engrg, 50, 2012:99-112
[2] Rodríguez-Millán, M. et al., Mat Des, 110, 2016:391-403
We would like to thank Julia Clarin, Fred Sebastian, Ana Vargas, and Sean Harrington. We would also like to thank the NU Center for STEM Education; particularly Claire Duggan, Jennifer Love, Claire Stipp, Yassine Souabny, Nicolas Fuchs, and Mary Howley. Funding for this project was provided by the United States Army Research Lab Soldier Protection Program Cooperative Agreement #W911NF2120208.
D'mitra Mukasa1, Michael Marchev1, Turner Jennings2, Sinan Müftü2, Rouzbeh Amini2,3
The padding is compressed by the weight of the helmet (A).
The padding is further compressed by buckling the chinstrap (B).
The padding is fully compressed when bullet hits the helmet (C).
Collect contact pressure data from military personnel
Create new helmet fitting simulations with pad pre-compression data considered
1 Young Scholars Program, Northeastern University, Boston, MA
2 Department of Mechanical and Industrial Engineering, Northeastern University, Boston, MA
3 Department of Bioengineering, Northeastern University, Boston, MA
This poster contains unpublished confidential information
(A)
(B)
Simulated top pad contact pressure difference between (A) 0.5 mm and (B) 1.5 mm padding compression
Helmet assembled with contact pressure sensors
Diagram of pressure sensors calibration setup
Plot of top pad contact pressure against the non-dimensionalized ratio of head width to helmet width of users wearing the chinstrap
Plot of top pad contact pressure against the non-dimensionalized ratio of head circumference to helmet circumference of users wearing the chinstrap
Representative calibration curves of pressure sensors mapping voltage output to pressure
There is a weak positive correlation between top pad contact pressure and the relative size of the helmet compared with the head (width and circumference ratio of head/helmet). When calibrating different helmet pads, we saw significant variation in the calibration curves. All helmet pads were assigned either a linear or piecewise non-linear calibration curve. We hypothesize that the difference among pad calibrations may be due to differing curvature of the helmet underneath the padding.
Male contact pressure is not significantly higher than females when the chinstrap is not applied. The pressure difference is statistically significant (p<.05) when the chinstrap is applied. We hypothesize that the difference between male and female pressures could be a result of smaller head and helmet sizes, since all the female participants sampled used either size S or M helmets. We further hypothesize that the increased difference from strapped data could indicate that males fasten the strap more tightly than females. Among all groups, we additionally found significantly higher strapped than unstrapped contact pressures. The sample size of the present study was limited to 18 participants, the results can be further refined by expanding the number of users tested.
Comparison of top pad contact pressure between user wearing and not wearing the chinstrap
Comparison of top pad contact pressure between male and female users while wearing the chinstrap
Comparison of top pad contact pressure between male and female users not wearing the chinstrap
Representative diagram of helmet padding layout

## Slide 17: Additional Lab Summary – Pregnant Valve Mechanics
Pregnancy increase risk of regurgitation
1.6M
Moderate to severe cases in the US1
US adults with mild TR1
15%
Tricuspid Regurgitation (TR)
Head/Helmet Contact Force Characterization in Combat Helmet Systems
NEU Young Scholars Program 2023 - August 3, 2023
Notes: While working in Prof. Rouzbeh Amini's lab, we worked on several projects in addition to our main research with combat helmets. Namely, we worked heavily on Julia Clarin's lab examining the effects of pregnancy on the tricuspid valve
During pregnancy the volume of blood increases and can cause blood regurgitation if the tricuspid valve does not close fully, causing the heart to pump harder than needed

## Slide 18: Discussion/Conclusion
Higher contact pressure among males
  Females tested had generally smaller heads and helmets
  Shape difference
Male/Female difference increase with strap application
  Magnification of the same difference
  Males may tension the strap more tightly
Higher contact pressure with tighter fit
  Pads forced to compress further
Sample consisted of 18 inexperienced users and may not be representative.
Head/Helmet Contact Force Characterization in Combat Helmet Systems
NEU Young Scholars Program 2023 - August 3, 2023
 |  | Percentiles |  |  |  | 
Sample |  | 1st | 5th | 50th | 95th | 99th
Male | [cm] | 18.3 | 18.8 | 20.0 | 21.1 | 21.7
Female | [cm] | 17.5 | 18.0 | 19.1 | 20.2 | 20.7
Head length population distribution
Source: DOD Human Factors Engineering