## Slide 1
2026-09-29
Richard West
Teach a Computer Chemistry, then Watch It React.

## Slide 3
Notes: o We used to build models to check our understanding;
♣ if we can’t make the model match the experiment then the understanding we built the model on (eg first order wrt O2) needs revising.
o May not be based on correct understanding – even if it fits the curve, it may not be physically meaningful.
o Not reliably predictive for conditions outside range of experiments, due to the complex T,P-depnedence mentioned above.
♣ Very difficult to do experiments at relevant conditions – too hot, high pressure, too fast (TiO2)
o Complex tradeoffs, competing pathways
o Strange temperature and pressure dependencies
♣ At higher temperature, a new dominant pathway may open up and the reaction order may change
♣ At higher pressure, a different pressure-dependent network may activate

## Slide 7: Predictive Detailed Kinetic Modeling
new conditions
chemical reactions
thousands
computer

## Slide 8: Using computers to predict how things will react.
Faster than experiments
Hypothetical scenarios
Transferrable skills
Efficient combustion of new fuels
Environmentally friendly flame suppressants
Destroying toxic “forever chemicals”
Catalytic synthesis of fuels and chemicals
Electrochemical synthesis of fuels and chemicals
Why?
What?

## Slide 9: Combustion Chemistry is Complex
Fuels are hard but routine
Halocarbons are weird!
0.48
0.53
0.57
0.67
0.79
0.92
ɸ=1.00
ɸ=0.67
0.57
0.53
0.62
CH2=CBrCF3
CF3Br
methane flame speed
suppressant fraction

## Slide 10: Combustion Chemistry is Complex
Fuels are hard but routine
Halocarbons are weird!
0.48
0.53
0.57
0.67
0.79
0.92
ɸ=1.00
ɸ=0.67
0.57
0.53
0.62
CH2=CBrCF3
CF3Br
methane flame speed
suppressant fraction

## Slide 11: Combustion Chemistry is Complex
Fuels are hard but routine
Halocarbons are weird!
0.48
0.53
0.57
0.67
0.79
0.92
ɸ=1.00
ɸ=0.67
0.57
0.53
0.62
CH2=CBrCF3
CF3Br
methane flame speed
suppressant fraction

## Slide 12: Combustion Chemistry is Complex
Fuels are hard but routine
Halocarbons are weird!
0.48
0.53
0.57
0.67
0.79
0.92
ɸ=1.00
ɸ=0.67
0.57
0.53
0.62
CH2=CBrCF3
CF3Br
methane flame speed
suppressant fraction

## Slide 13: Halogenated Hydrocarbons (HHCs) are commonly used as refrigerants and flame suppressants
https://learn.compactappliance.com/freon-alternatives/
http://amerex-fire.com/products/halon-1211-extinguishers/
CF2ClBr
C2HF5
CH2F2
F3CCH2F
Halon 1211
Notes: 2. First off, what are HHCs used for? HHCs are widely uses as refrigerants and as flame suppressants. For example, Refrigerant 407c which is used in air conditioning systems is primarily a mixture of 3 fluorinated hydrocarbons. CF2ClBr, more commonly known as Halon 1211, is a fire suppressant often used aboard commercial aircrafts

## Slide 14: Environmental concerns motivate a new generation of HHC flame suppressants and refrigerants
Compound | Formula | Ozone Depleting Potential [2] | Lifetime (years) | Global Warming Potential [3]
CFC-12 | CCl2F2 | 0.82 | 100 | 10,200
CFC-113 | CCl2FCClF2 | 0.85 | 85 | 5,820
CFC-11 | CCl3F | 1 | 45 | 4,660
HCFC-22 | CHClF2 | 0.04 | 11.9 | 1,760
HFC-134a | CH2FCF3 | 0.000015 | 13.4 | 1,300
Carbon dioxide | CO2 | 0 | 2-20,000[4] | 1
HFO-1234yf | CF3CF=CH2 | 0 | 0.03 | <1
1st Gen
2nd Gen
3rd Gen
How CFC-11 destroys the ozone layer [1]
[1] http://www.theozonehole.com/ozonedestruction.html
[2] EPA. https://www.epa.gov/ozone-layer-protection/ozone-depleting-substances
Notes: HHC fire suppressants are good at putting out fires, but they are harmful to the environment. The first generation of suppressants, chlorofluorocarbons or CFCs, were potent greenhouse gases and depleted the ozone layer, as shown on the figure in the upper left. A simplified animation of how this happened is shown below.
In the stratosphere, the Carbon-Chlorine bond in CFC dissociates with the absorbance of UV light creating free chlorine radicals. The chlorine radicals abstract an oxygen atom from ozone creating molecular oxygen. The destruction of the ozone layer by CFCs led to the development of a second generation of suppresants, mainly HCFCs and HFCs. Although these suppressants are ozone-friendly, they are strong greenhouse gases with global warming potentials over 1000 times that of carbon dioxide(GWP is defined as the warming potential over a chosen amount of time of 1 kg of a gas relative to 1 kg of CO2, which is given a GWP value of 1). These environmental concerns motivate the need for a new generation of greener and cleaner HHC refrigerant and flame suppressants.
One Dobson Unit is the number of molecules of ozone that would be required to create a layer of pure ozone 0.01 millimeters thick at a temperature of 0 degrees Celsius and a pressure of 1 atmosphere (the air pressure at the surface of the Earth). Expressed another way, a column of air with an ozone concentration of 1 Dobson Unit would contain about 2.69x1016ozone molecules for every square centimeter of area at the base of the column
GWP is defined as the warming potential over a chosen amount of time of 1 kg of a gas relative to 1 kg of CO2, which is given a GWP value of 1.

## Slide 15: Environmental concerns motivate a new generation of HHC flame suppressants and refrigerants
Compound | Formula | Ozone Depleting Potential [2] | Lifetime (years) | Global Warming Potential [3]
CFC-12 | CCl2F2 | 0.82 | 100 | 10,200
CFC-113 | CCl2FCClF2 | 0.85 | 85 | 5,820
CFC-11 | CCl3F | 1 | 45 | 4,660
HCFC-22 | CHClF2 | 0.04 | 11.9 | 1,760
HFC-134a | CH2FCF3 | 0.000015 | 13.4 | 1,300
Carbon dioxide | CO2 | 0 | 2-20,000[4] | 1
HFO-1234yf | CF3CF=CH2 | 0 | 0.03 | <1
1st Gen
2nd Gen
3rd Gen
How CFC-11 destroys the ozone layer [1]
[1] http://www.theozonehole.com/ozonedestruction.html
[2] EPA. https://www.epa.gov/ozone-layer-protection/ozone-depleting-substances
Notes: HHC fire suppressants are good at putting out fires, but they are harmful to the environment. The first generation of suppressants, chlorofluorocarbons or CFCs, were potent greenhouse gases and depleted the ozone layer, as shown on the figure in the upper left. A simplified animation of how this happened is shown below.
In the stratosphere, the Carbon-Chlorine bond in CFC dissociates with the absorbance of UV light creating free chlorine radicals. The chlorine radicals abstract an oxygen atom from ozone creating molecular oxygen. The destruction of the ozone layer by CFCs led to the development of a second generation of suppresants, mainly HCFCs and HFCs. Although these suppressants are ozone-friendly, they are strong greenhouse gases with global warming potentials over 1000 times that of carbon dioxide(GWP is defined as the warming potential over a chosen amount of time of 1 kg of a gas relative to 1 kg of CO2, which is given a GWP value of 1). These environmental concerns motivate the need for a new generation of greener and cleaner HHC refrigerant and flame suppressants.
One Dobson Unit is the number of molecules of ozone that would be required to create a layer of pure ozone 0.01 millimeters thick at a temperature of 0 degrees Celsius and a pressure of 1 atmosphere (the air pressure at the surface of the Earth). Expressed another way, a column of air with an ozone concentration of 1 Dobson Unit would contain about 2.69x1016ozone molecules for every square centimeter of area at the base of the column
GWP is defined as the warming potential over a chosen amount of time of 1 kg of a gas relative to 1 kg of CO2, which is given a GWP value of 1.

## Slide 16: Environmental concerns motivate a new generation of HHC flame suppressants and refrigerants
Compound | Formula | Ozone Depleting Potential [2] | Lifetime (years) | Global Warming Potential [3]
CFC-12 | CCl2F2 | 0.82 | 100 | 10,200
CFC-113 | CCl2FCClF2 | 0.85 | 85 | 5,820
CFC-11 | CCl3F | 1 | 45 | 4,660
HCFC-22 | CHClF2 | 0.04 | 11.9 | 1,760
HFC-134a | CH2FCF3 | 0.000015 | 13.4 | 1,300
Carbon dioxide | CO2 | 0 | 2-20,000[4] | 1
HFO-1234yf | CF3CF=CH2 | 0 | 0.03 | <1
1st Gen
2nd Gen
How greenhouse gasses cause global warming [1]
[1] https://www.museumoftheearth.org/changing-climate/greenhouse-effect
[2] EPA. https://www.epa.gov/ozone-layer-protection/ozone-depleting-substances
[3] https://cen.acs.org/articles/91/i34/Halocarbons-Reassessed.html and Hodnebrog et al. Rev. Geophys. 2013, DOI: 10.1002/rog.20013
[4] Archer, et al. (2009). Atmospheric Lifetime of Fossil Fuel Carbon Dioxide. Annual Review of Earth and Planetary Sciences, v.37, 117-134 (2009).
Notes: HHC fire suppressants are good at putting out fires, but they are harmful to the environment. The first generation of suppressants, chlorofluorocarbons or CFCs, were potent greenhouse gases and depleted the ozone layer, as shown on the figure in the upper left. A simplified animation of how this happened is shown below.
In the stratosphere, the Carbon-Chlorine bond in CFC dissociates with the absorbance of UV light creating free chlorine radicals. The chlorine radicals abstract an oxygen atom from ozone creating molecular oxygen. The destruction of the ozone layer by CFCs led to the development of a second generation of suppresants, mainly HCFCs and HFCs. Although these suppressants are ozone-friendly, they are strong greenhouse gases with global warming potentials over 1000 times that of carbon dioxide(GWP is defined as the warming potential over a chosen amount of time of 1 kg of a gas relative to 1 kg of CO2, which is given a GWP value of 1). These environmental concerns motivate the need for a new generation of greener and cleaner HHC refrigerant and flame suppressants.
One Dobson Unit is the number of molecules of ozone that would be required to create a layer of pure ozone 0.01 millimeters thick at a temperature of 0 degrees Celsius and a pressure of 1 atmosphere (the air pressure at the surface of the Earth). Expressed another way, a column of air with an ozone concentration of 1 Dobson Unit would contain about 2.69x1016ozone molecules for every square centimeter of area at the base of the column
GWP is defined as the warming potential over a chosen amount of time of 1 kg of a gas relative to 1 kg of CO2, which is given a GWP value of 1.

## Slide 17: Environmental concerns motivate a new generation of HHC flame suppressants and refrigerants
1st Gen
2nd Gen
3rd Gen
Why a flammable “flame suppressant” is a bad idea [1]
[1] The Simpsons, Season 11, Episode 22
[2] EPA. https://www.epa.gov/ozone-layer-protection/ozone-depleting-substances
[3] https://cen.acs.org/articles/91/i34/Halocarbons-Reassessed.html and Hodnebrog et al. Rev. Geophys. 2013, DOI: 10.1002/rog.20013
[4] Archer, et al. (2009). Atmospheric Lifetime of Fossil Fuel Carbon Dioxide. Annual Review of Earth and Planetary Sciences, v.37, 117-134 (2009).
Compound | Formula | Ozone Depleting Potential [2] | Lifetime (years) | Global Warming Potential [3]
CFC-12 | CCl2F2 | 0.82 | 100 | 10,200
CFC-113 | CCl2FCClF2 | 0.85 | 85 | 5,820
CFC-11 | CCl3F | 1 | 45 | 4,660
HCFC-22 | CHClF2 | 0.04 | 11.9 | 1,760
HFC-134a | CH2FCF3 | 0.000015 | 13.4 | 1,300
Carbon dioxide | CO2 | 0 | 2-20,000[4] | 1
HFO-1234yf | CF3CF=CH2 | 0 | 0.03 | <1
Notes: HHC fire suppressants are good at putting out fires, but they are harmful to the environment. The first generation of suppressants, chlorofluorocarbons or CFCs, were potent greenhouse gases and depleted the ozone layer, as shown on the figure in the upper left. A simplified animation of how this happened is shown below.
In the stratosphere, the Carbon-Chlorine bond in CFC dissociates with the absorbance of UV light creating free chlorine radicals. The chlorine radicals abstract an oxygen atom from ozone creating molecular oxygen. The destruction of the ozone layer by CFCs led to the development of a second generation of suppresants, mainly HCFCs and HFCs. Although these suppressants are ozone-friendly, they are strong greenhouse gases with global warming potentials over 1000 times that of carbon dioxide(GWP is defined as the warming potential over a chosen amount of time of 1 kg of a gas relative to 1 kg of CO2, which is given a GWP value of 1). These environmental concerns motivate the need for a new generation of greener and cleaner HHC refrigerant and flame suppressants.
One Dobson Unit is the number of molecules of ozone that would be required to create a layer of pure ozone 0.01 millimeters thick at a temperature of 0 degrees Celsius and a pressure of 1 atmosphere (the air pressure at the surface of the Earth). Expressed another way, a column of air with an ozone concentration of 1 Dobson Unit would contain about 2.69x1016ozone molecules for every square centimeter of area at the base of the column
GWP is defined as the warming potential over a chosen amount of time of 1 kg of a gas relative to 1 kg of CO2, which is given a GWP value of 1.

## Slide 18: Current and potential suppressants and refrigerants are halogenated hydrocarbons
 | Suppressants | Refrigerants
Current | CF3Br CF2ClBr | CH2F2 CF3CHF2 CF3CH2F
Potential | CH2=CBrCF3 (2-BTP) CHF2CF3, CF3CHCl2, CF3H, C2F5H, C3F7H | CH2=CFCF3 CH2=CHCF3 CHF=CFCF3 CHF=CFCH3
Notes: 4. This chart shows come current suppressants and refrigerants, and many greener ones currently being tested and researched. Lets take a closer look at the combustion properties of two of these suppressants, a current one CF3Br and a greener alternative 2-BTP.

## Slide 19: 2-BTP Combustion is remarkable and complex with multiple competing pathways
Reaction Pathway of 2-BTP decomposition [1]
2-BTP
[1] Babushok, V. I., Linteris, G. T., Burgess, D. R., & Baker, P. T. (2015). Hydrocarbon flame inhibition by C3H2F3Br (2-BTP). Combustion and Flame, 162(4), 1104–1112. https://doi.org/10.1016/j.combustflame.2014.10.002
[2] Drage, E. A., Jaksch, D., Smith, K. M., McPheat, R. A., Vasekova, E., & Mason, N. J. (2006). Journal of Quantitative Spectroscopy and Radiative Transfer, 98(1), 44–56. https://doi.org/10.1016/j.jqsrt.2005.05.071
[3] U.N. Environment Program. https://ozone.unep.org/system/files/documents/HTOC_technical_note1_2018.pdf
 | Status | Ozone Depleting Potential | Global Warming Potential
CF3Br | Current | 15.9 | 5800 [2]
2-BTP | Potential | 0.0028 | 0.26 [3]
0.48
0.53
0.57
0.67
0.79
0.92
ɸ=1.00
ɸ=0.67
0.57
0.53
0.62
2-BTP
CF3Br
CH2=CBrCF3
Normalized burning velocity of methane/air flame
Suppressant volume fraction
Notes: 5. The figure on the left shows the flame speeds of methane/oxygen mixtures with respect to volume fractions of the flame suppressants (CF3Br in red and 2-BTP in green). The current suppressant CF3Br behaves as a flame suppressant should. It slows down flame propagation as you add more suppressant. The behavior of 2-BTP is more complex. At low volume fractions, it slows down the flame. However, as you add more 2-BTP, the flame either continues to slow down or speeds up depending on the flame mixture. To understand and predict the unusual behavior of 2-BTP and other potential HHC suppressnats, we need to understand its complicated reaction mechanism with multiple intermediates and competing pathways.

## Slide 20: Detailed kinetic modeling is complex
For each chemical reaction
we need:
  forward rate coefficient
  equilibrium constant

## Slide 21: Computational Chemistry has two sides
Learning from the computer
Teaching to the computer

## Slide 22
Learning chemistry from the computer

## Slide 23: Energies can be found ab initio using quantum chemistry
Solve the Schrödinger wave equation for E.
Can’t solve exactly for multi-electron molecules.
Modern methods give useful results in reasonable time.
Notes: The Eigenvalue of the molecular Hamiltonian operator gives the energy of the molecule.
What’s the Hamiltonian operator? big and complicated, but if we pretend the nuclei are in fixed positions, which relative to the speed of the electrons, they pretty much are, we are left with:
the kinetic energy of the electrons, the electric potential energy of the nuclei repelling each other, the potential energy of the electrons in the fixed electric field caused by the nuclei, and the potential energy of the electrons in the electric field caused by the other electrons. This is a problem as we don’t yet know where the other electrons are!
Schrodinger equation can’t be solved for more than one electron, and We have hundreds.
DFT
Nice editorial by Walter Thiel: http://bit.ly/Thiel

## Slide 24: Quantum calculations can provide a lot of things:
Pretty pictures
Electronic energy
Geometry optimization
Rotational constants
Vibrational frequencies
Find temperature variation of Cp, H, S through Statistical Mechanics
Notes: pretty pictures
this is the Highest Occupied Molecular orbital of the dimer (Ti2O2Cl4)
..and here are the other 63 occupied orbitals. Alhough they’re less pretty, they all contribute to the electronic energy of the molecule.
Now we can calculate the energy of a bunch of atoms arranged in the shape of a molecule, we can use this to optimize this shape. The geometry with the lowest energy is most like the real geometry.
Now we can also calculate the 3 rotational frequencies, and in this case 18 vibrational modes of the molecule.

## Slide 25
Teaching chemistry to the computer

## Slide 26: Automatic reaction mechanism generation needs methods to:
Represent molecules (and identify duplicates)
Create reactions (and then new species)
Estimate thermodynamic and kinetic parameters (quickly!)
Choose which reactions to include
Notes: figure out names :)

## Slide 27: Molecules are represented as graphs
CH3CH2.
C
C*
H
H
H
H
H
=

## Slide 28: Reaction families propose all possible reactions with given chemical species
Template for recognizing reactive sites
Recipe for changing the bonding at the site
bond breaking and
hydrogen abstraction
intramolecular
H-abstraction

## Slide 29: Reaction families propose all possible reactions with given chemical species
Template for recognizing reactive sites
Recipe for changing the bonding at the site

## Slide 30: There are usually many pathways

## Slide 31: Some pathways go further than others

## Slide 32: Faster pathways are explored further
Slower pathways are ignored
A
B
C
D
E
F
G
H
A
B
C
D
E
F

## Slide 33: Thermochemistry is (often*) estimated by Benson group contributions
C-(C)(H)3
C-(C)2(H)2
Cb-(H)
C-(C)(Cb)(O)(H)
*we also have big libraries, and graph convolution neural networks, etc.
Notes:   Molecule is broken into ‘groups’ of atoms
  Each group contributes a known amount to the properties

## Slide 34: Parameter estimates are based on the local structure of the reacting sites
*we also have big libraries, and graph convolution neural networks, etc.

## Slide 35: Model “edge” can be huge
100 species
1000 reactions
15,000 species
180,000 reactions
Notes: show that 180,000 is a lot. (number of __ in __)

## Slide 36: We can do the same for heterogeneous catalysis
or
or
Adsorbate Database
Gas phase Database
Gas phase Estimator
Pt(111) Adsorbate
Any Adsorbate
Gas phase
Species
∆ Binding Energy
Adsorption Estimator
XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX
XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX
LSR
+
+

## Slide 37
Learning more chemistry from the computer

## Slide 38
How does it react?
Which catalyst is best?
Why?

## Slide 39: Exascale Catalytic Chemistry uses fast computers (1 ExaFLOP = 1,000,000,000,000,000,000 FLOPS)
Notes: Aurora has 64k GPUS and almost 2 exaflops peak performance

## Slide 40: Current projects
Halocarbon Combustion
PFAS incineration
Heterogeneous Catalysis
Electrocatalysis
Pharmaceutical Synthesis
Hydrogen Embrittlement
Siloxane Degradation
Combustion Cyberinfrastructure

## Slide 41: M.S. Research Alumni – 2016 to 2018
Name | Rasha Atwi | Krishna Sirumalla | Priyanka Satpute | Shenghui Qin | Chikpezili Ajulu | Mingyu Wan
Before | B.E. ChE, Am. Univ. of Beirut | B.S. ChE, India | B.S. ChE, MIT | M.S. Safety Eng., Nanjing Tech Univ. | B.S. MechE, Northeastern | B.Eng. Energy Eng., North Univ. of China
Research | N-heterocycle formation in algae liquefaction | CNNs for predicting chemical kinetics [DNF thesis] | RMG-Electrocat for solid oxide fuel cell kinetics | Autoignition kinetics of n-heptane blends | Automated kinetic mechanisms for Fischer-Tropsch fuels | Reaction Mechanism Generation, project [DNF thesis]
Next | Ph.D. ChE, Stony Brook | Ph.D. ChE, Northeastern | Senior Consultant, Navigant / Guidehouse | Ph.D. ChE, U. Pittsburgh cancelled (COVID) | Engineer, DNV | Ph.D. ChE, UMass Lowell
Now | Research Scientist, Biogen | Senior Research Scientist ML, Iambic Therapeutics | Associate Director, Guidehouse | China | System Simulation Specialist, Cummins | Assistant Professor, Wuhan Univ. of Sci. & Tech.

## Slide 42: M.S. Research Alumni – 2018 to today
Name | Chao Xu | Ting-Chen Lee | Sevy Harris | Kian Mehrabani | Danielle Lucey | You?
Before | B.S. Chemistry, Dalian Jiaotong U | B.S. ChE, Chung Cheng Inst. of Tech. | B.S. EE Ohio State, M.S. EE Stanford | B.S./M.S. ChE, Northeastern (PlusOne) | B.A. Chemistry & Math, Colby College | 
Research | ChemCheck: a debugging tool for kinetic models | RMG for heterogeneous ammonia oxidation | Uncertainty quantification for microkinetic models [DNF thesis] | Database & web app for detailed kinetic models | Pathways of catalytic CO2 hydrogenation [DNF thesis] | 
Next | Ph.D. ChE, Northeastern | R.O.C. Army | Ph.D. ChE, Northeastern | Data Engineer | Ph.D. ChE, Northeastern | 
Now | Senior Data Scientist, Amgen | Ph.D. National Cheng Kung University, Taiwan | Ph.D. awarded Aug 2026 | Data Engineer, Spotify | Ph.D. student, Northeastern | 

## Slide 43
Notes: This is the computer model Gordon and McBride used when they devised the NASA polynomial format
for thermochemistry (now used in CHEMKIN). It was designed to fit on 80-column punch-cards.

## Slide 44: NASA (Chemkin) format is very dense – not much room for species identifiers
Chemical Formula
Parameters for H(T), S(T)
Species Name

## Slide 45: Space constraints led to “creative” naming schemes
Notes: Notice hydroperoxypropan-2-one has two different names, often in the same mechanism file!

## Slide 46: Sometimes the same species appears twice in a model, with different names
C3KET21 is generated from alkyl peroxy radical isomerization pathway
CH3COCH2O2H is generated from low-temperature oxidation of acetone
Notes: Notice hydroperoxypropan-2-one has two different names, often in the same mechanism file!

## Slide 47: We need a tool to help identify species

## Slide 48: Reaction Mechanism Generator (RMG-Py) has many of the required features
Represent molecules and recognize duplicates
Propose reactions from templates and rules
Estimate parameters quickly
Expand model based on known species
Modular and Extensible!

## Slide 49: Algorithm is like solving a Sudoku puzzle.
Identify species with only one possible structure
        CO2
        H2O
        C3H8
Then species with "borrowed" thermochemistry
Then “boot-strap” based on how these react…

## Slide 50: Identifying ‘sc3h5co’ from its reactions:
Notes: The first 6 reactions are all H-abstractions giving 4 possibilities for sc3h5co.
The 7th reaction is beta-scission, also giving 4 possibilities.

## Slide 51: Identifying ‘sc3h5co’ from its reactions:
but-2-enoyl
Notes: By considering all seven reactions, we can deduce the most likely isomer.

## Slide 52: Human-Computer team can identify species more quickly
Our tool uses RMG to generate reactions to compare with the target model
A human reviews the evidence and confirms matches.

## Slide 53
Notes: Identified 14,443 species from 65 models

## Slide 54
      .edu/comocheng
Richard H. West r.west@neu.edu Grant No. 1403171, 2531937

## Slide 55: Ph.D. Graduates
Dr. Pierre Bhoorasingh | Dr. Fariba Khanshan | Dr. Belinda Slakman | Dr. Nate Harms | Dr. Krishna Sirumalla | Dr. Emily Mazeau | Dr. David Farina
Senior Applied Scientist | Associate Director Pharmacometrician | Senior ML Scientist | Senior Data Scientist | Senior Research Scientist ML | Postdoctoral Research Associate | ML Research Scientist II,
Amazon | Novartis | Relay Therapeutics | Valo Health | Iambic Therapeutics | Oak Ridge National Laboratory | Iambic Therapeutics
BS ChBE MIT, MS BioE UPenn | BS ChE, Persian Gulf U | BS ChE, Princeton | BS ChE, Oregon State U | BS ChE, India | BS ChE, RPI | BS Chemistry Boston College
 | https://www.linkedin.com/in/fariba-khanshan-b404a28a/ | https://www.linkedin.com/in/belindaslakman/ |  |  |  | 

## Slide 56: R.West@northeastern.edu

## Slide 57: How else can I help you?
Global Sensitivity Analysis
    identify causes of uncertainty
Bayesian Parameter Estimation
    sophisticated regression
Research Software Engineering
    trustworthy, reusable, accessible